## Slide 1: All-in-one Home ESS
All-in-one Home Energy Storage Systems
2.94kW ~ 11.76kW

## Slide 2
1. Built-in various protection functions
Built-in smart BMS provides overcharge, over-discharge, and
over-current protection functions
2. Durability and reliability
Maintains long life and stable performance
without 3-year cycle battery replacement
3. Built-in remote monitoring and management function
Battery status, voltage, current, temperature, etc.
can be applied in real-time
4. Convenient maintenance management Remote management through
WIFI connection reduces system maintenance costs
5. Safe and efficient battery cell management function
Removable design by cell allows the replacement of only defective cells
Key Features

## Slide 3
1. Environmentally friendly and low maintenance
2. Easy to install: ALL-IN-ONE design for easy movement and installation
3. High output and long life: over 5,000 charge/discharge cycles
4. Multipurpose: Optimized for solar ESS, ships, UPS, etc.
5. Predictive maintenance support: AI-based analysis predicts battery status
in advance and allows immediate replacement
system connection diagram

## Slide 4
2.94 kW
5.88 kW
11.76 kW
Features
Removable Battery capacity expansion
1. The battery can be easily removed and reattached
2. Individual batteries can be monitored, allowing easy replacement of only worn-out batteries
3. Real-time battery status measurement possible through smartphone or PC central monitoring
4. Can be used as a replacement for the distribution panel rectifier
5. Charging is possible through solar power generation
6. Supports AC output (AC220V 50/60Hz)
7. Supports wireless WIFI

## Slide 5
Details of All-in-one
2.94KW for Home Energy Storage System
⑭
⑩
⑪
⑫
⑬
15
16
17
19
18
LCD Display
14-1
1 AC indicator
2. Inverter indicator
3. Charge indicator
4. Error indicator
5. LCD
6. ESC button
7. UP button
8. DOWN button
9. ENTER button
button | explanation
ESC | Exit setup mode
UP | Go to previous selection
DOWN | Go to next choice
ENTER | Confirm selection in setup mode or enter setup mode
LED indicator |  |  | message
① AC | Status indicator (green) | Steady on | main power is normal and the main power is supplied
 |  | blinking | Main power is normal, but main power is not being supplied
 |  | Power off | Main power is abnormal
② Inverter | Inverted indicator (yellow) | Steady on | Output is powered by battery or PV in battery mode
 |  | Power off | other states
③ Charging | Charging indicator (yellow) | Steady on | Battery is floating and charging
 |  | blinking | The battery is charging at a constant voltage
 |  | Power off | other states
④ Fault | Error indicator (red) | Steady on | An error occurred in the inverter
 |  | blinking | Alert occurs in inverter
 |  | Power off | The inverter is operating normally.
10. WiFi ANT
11. Solar MPPT input_(for battery charging)
12. AC 220V input_(for battery charging)
ON/OFF switch
13. Fan
14. AC 220V output X 2
14-1 output_(terminal for + -battery charging)
15. Ground case GND
16. DC 12V input
(battery connection terminal)
17. 4S BMS 230A module
18. Inverter ON/OFF switch
19. Removable cell battery

## Slide 6
6kw Specification
Items | Specification | Remarks
INPUT Charging | Solar MPPT Input current 15A, Solar Charging Current 100A AC : 220-230v, Charing Current 80A | 
Battery | LiFePO4 Battery 3.2V 230A Size : 173mm x 203mm x 54mm Weight: 4.1kg Charging method: CC/CV Operating temperature: -25 ~ 55°C | 
BMS | BMS 4S1P 12.8V x 230A =2.94KW | BMS : Battery Management System
Battery Module | Module Voltage : 4EA x 3.2V x 230A =12.8V (2.94KW) Replaceable for each removable cell CTPS and BMS are interconnected to provide temperature notification and cell balance function for each cell | CTPS : Cell Temperature Protective System
Output of Power | Inverter AC 220-230V Frequency 50/60hz, pure sine wave Capacity : 2KW | 
Size | 484x 526 x 351mm (WxHxD) | 
Weight | 40.0 kg | 
Communication | WiFi | 
Etc | Option: Each cell voltage, temperature, SOH, DOD | SOH : Status of Health DOD : Depth of Discharge
Main HESS
Auxiliary battery

## Slide 7
Model | SHE01-3K | SHE01-6K | SHE01-12K
Capacity Battery | main (1 SET) 2.94kW | auxiliary battery 1SET 5.88kW | auxiliary battery 3SET 11.76kW
Details |  |  | 
Battery | LiFePO4 Battery 3.2V 230A Size : 174mm x 203mm x 54mm Weight: 4.1kg Charging method: CC/CV Operating temperature: -25 ~ 55°C | LiFePO4 Battery 3.2V 230A Size : 174mm x 203mm x 54mm Weight: 4.1kg Charging method: CC/CV Operating temperature: -25 ~ 55°C | LiFePO4 Battery 3.2V 230A Size : 174mm x 203mm x 54mm Weight: 4.1kg Charging method: CC/CV Operating temperature: -25 ~ 55°C
BMS | 4S 1P 12.8V/ 230A | 4S 2P 25.6V /230A | 4S 4P 51.2V / 230A
Battery Module | Module Voltage : 4EA x 3.2V Replaceable for each removable cell CTPS (option) | Module Voltage : 8EA x 3.2V Replaceable for each removable cell CTPS (option) | Module Voltage:16EA x 3.2V Replaceable for each removable cell CTPS (option)
Output of Power | Inverter AC 220-230V Frequency 50/60hz, pure sine wave Capacity : 2KW | Inverter AC 220-230V Frequency 50/60hz, pure sine wave Capacity : 4KW | Inverter AC 220-230V Frequency 50/60hz, pure sine wave Capacity : 6KW
Size | 484x 526 x 351mm (WxHxD) | 694x 526 x 351mm (WxHxD) | 1.114x 526 x 351mm (WxHxD)
Weight | 40.0 kg | 55.0 kg | 95.0 kg
Communication | WIFI | WIFI | WIFI
Etc | Option: Each cell voltage, temperature, SOH, DOD | Option: Each cell voltage, temperature, SOH, DOD | Option: Each cell voltage, temperature, SOH, DOD
Capacity 4-Type, Specification