## Slide 1: All-in-one Home ESS
2.6kW ~ 10kW
All-in-one Home Energy Storage Systems

## Slide 2
주요 특징
다양한 보호기능 내장
스마트 BMS 내장으로 과충전, 과방전, 과전류 보호 기능 제공
내구성과 신뢰성
2,3년 주기 배터리 교체 없이 긴 수명과 안정적인 성능 유지
원격모니터링 및 관리기능 내장
배터리 상태, 전압, 전류,온도 등을 실시간으로 적용 가능
편리한 유지보수관리
WIFI연결을 통한 원격관리, 시스템 유지 비용 절감
안전하고 효율적인 배터리셀관리기능
셀별 착탈식 설계로 불량 셀 만 교체 가능

## Slide 3
시스템 연결도
친 환경적이고 유지보수가 적음
설치 용이성 : ALL-IN-ONE 설계로 이동 및 설치가 용이
고출력 및 긴 수명 15.000회 이상의 충.방전 사이클 가능
다목적 활용 가능 : 태양광 ESS, 선박용,통신서버,병원, UPS,기타 등에 최적화
예측 유지 보수 지원 가능 : AI 기반 분석으로 배터리 상태를 사전 예측 즉시교환 가능
Emergency
Generater

## Slide 4
착탈식 용량 확장
외형도
배터리를 착탈식으로 쉽게 탈부착이 가능함
개별 배터리를 감시하여 노후화된 배터리만 손쉽게 교체 가능
스마트폰 또는 PC중앙 감시를 통하여 실시간 배터리 상태 계측 가능
수배전반 정류기반을 대체하여 사용가능
태양광 발전을 통한 충전도 가능
AC / DC출력을 지원 (AC220V or DC110V)
무선 WIFI지원
2.6 kW
5.2 kW
+
10 kW
Features

## Slide 5
Details of All-in-one
5KW for Home Energy Storage System
10. WIFI ANT 무선통신
11. 태양광 MPPT 입력_(Battery 충전용)
12. AC 220V입력_(Battery 충전용)
- ON/OFF Switch
13. FAN
14. AC 220V 출력 X 2ea(4.2KW)
14-1. DC 24/48V출력_(Battery 충전용 단자)
15. 접지 Case GND
16. DC 24/48V입력_(Battery 연결단자)
17. 8S BMS 200A 모듈
18. Inverter ON/OFF S/W
19.착탈식 셀 배터리
⑭
⑩
⑪
⑫
⑬
15
16
17
19
18
1. AC 표시기
2. 인버터 표시기
3. 충전 표시기
4. 오류 표시기
5. LCD 디스플레이
6. ESC 버튼
7. UP 버튼
8. DOWN 버튼
9. ENTER 버튼
LED 표시기 |  |  | 메세지
① AC | 상태표시 (녹색) | 계속 켜짐 | 주전원은 정상이고 주전원이 인입
 |  | 깜박거림 | 주전원은 정상이지만 주전원이 인입되고 있지않음
 |  | 전원 꺼짐 | 주전원이 비정상
② Inverter | 반전표시 (황색) | 계속 켜짐 | 출력은 배터리 또는 배터리모드에서 PV에 의해 구동
 |  | 전원 꺼짐 | 그 외 상태
③ Charging | 충전표시 (황색) | 계속 켜짐 | 배터리가 부동 충전 중
 |  | 깜박거림 | 베터리가 일정한 전압으로 충전 중
 |  | 전원 꺼짐 | 그 외 상태
④ Fault | 오류표시 (적색) | 계속 켜짐 | 인버터에 오류 발생
 |  | 깜박거림 | 인버터에 경고 발생
 |  | 전원 꺼짐 | 인버터가 정상적으로 작동 중
LCD Display
버튼 | 설명
ESC | 설정 모드를 종료하기
UP | 이전 선택으로 가기
DOWN | 다음 선택으로 가기
ENTER | 설정모드에서 선택을 확정하거나 설정모드 입력하기
14-1

## Slide 6
5kw Specification
Items | Specification | Remarks
INPUT Charging | Solar MPPT Input current 15A, Solar Charging Current 100A AC : 220-230v, Charing Current 80A | 
Battery | LFP Battery 3.2V 230A Size : 173mm x 203mm x 54mm Weight: 4.1kg Charging method: CC/CV Operating temperature: -25 ~ 55°C | 
BMS | BMS 4S1P 12.8V/230A = 2.94KW | BMS : Battery Management System
Battery Module | Module Voltage : 4EA x 3.2V x 230A =12.8V (2.94KW) Replaceable for each removable cell CTPS and BMS are interconnected to provide temperature notification and cell balance function for each cell | CTPS : Cell Temperature Protective System
Output of Power | Inverter AC 220-230V Frequency 50/60hz, pure sine wave Capacity : 2 KW | 
Size | 484x 526 x 351mm (WxHxD) | 
Weight | 40.0 kg | 
Communication | WiFi | 
Etc | Option: Each cell voltage, temperature, SOH, DOD | SOH : Status of Health DOD : Depth of Discharge
메인 HESS
보조 배터리

## Slide 7
모델 | SHE01-3 | SHE01-6 | SHE01-12
Capacity | 본체 (기본1SET) 2.94kW | 보조배터리 1SET 5.88kW | 보조배터리 3SET 11.76kW
Details |  |  | 
Battery | LFP Battery 3.2V 230A Size : 170mm x 203mm x 54mm Weight : 2kg Charging method : CC/CV Operating temperature : -25 ~ 55°C | LFP Battery 3.2V 230A Size : 170mm x 203mm x 54mm Weight : 2kg Charging method : CC/CV Operating temperature : -25 ~ 55°C | LFP Battery 3.2V 230A Size : 170mm x 203mm x 54mm Weight : 2kg Charging method : CC/CV Operating temperature : -25 ~ 55°C
BMS | 4S 1P 12.8V/230A | 4S 2P 25.6V/230A | 4S 4P 51.2V / 230A
Battery Module | Module = 2.94KW Voltage : 4EA x 3.2V Replaceable for each removable cell CTPS (option) | Module = 5.88KW Voltage : 8EA x 3.2V Replaceable for each removable cell CTPS (option) | Module = 11.76KW Voltage:16EA x 3.2V Replaceable for each removable cell CTPS (option)
Output of Power | Inverter AC 220-230V Frequency 50/60hz, pure sine wave Capacity : 2KW | Inverter AC 220-230V Frequency 50/60hz, pure sine wave Capacity : 4KW | Inverter AC 220-230V Frequency 50/60hz, pure sine wave Capacity : 6KW
Size | 484x 526 x 351mm (WxHxD) | 694x 526 x 351mm (WxHxD) | 1.114x 526 x 351mm (WxHxD)
Weight | 40.0 kg | 55.0 kg | 95.0 kg
Communication | WiFi | WiFi | WiFi
Etc | Option: Each cell voltage, temperature, SOH, DOD | Option: Each cell voltage, temperature, SOH, DOD | Option: Each cell voltage, temperature, SOH, DOD
용량별 Specification